## Slide 1: Cloud@eBay Overlay Networks
JC Martin – Cloud Architect (@jchmartin)

## Slide 2
Any Application, Anywhere

## Slide 3
Infra
Infra
Infra
Infra
Spare
spare
spare
spare
Application
App
App
App
Prod
QA
Exp.
Silos with custom design
Shared Infrastructure
Global resource pool
Application
App
App
App
Prod
QA
Exp.
Virtualized infrastructure
Virtual Environments

## Slide 4: Class of Service
Obligations | Restrictions | Capabilities
QA Approved Builds | No Login Access | Core DB access
Prod OS version | No Corp Access | 24/7 Incident Mgt
Monitoring | No QA Access | Site traffic Access
Production
Obligations | Restrictions | Capabilities
Certified OS versions | Limited Prod Access | Full root
 | Limited QA Access | 
 | No site Traffic | Filtered Internet
DEV
Obligations | Restrictions | Capabilities
 | No Prod Access | Private DB
Certified OS Versions | No Corp Access | 24/7 Incident Mgt
Monitoring | No QA Access | Site traffic Access
External

## Slide 5: Infrastructure designed for scale
Spine
Leaves
Core
M servers
2x1Gb
N leaves
4 spines
Flat L3 (all switches are routers too)
Line rate from any server to any server (oversubscription = 48/40)
OSPF/ECMP to advertise routes
(48x1Gb)
(Nx10Gb)
48 -> N “½ racks”

## Slide 6: Isolation options : L2
Production
QA
VLAN trunk
vlan 1
vlan n
QA
Prod
Dedicated Network
VLAN Based
- physical network build out
- Fragmentation
- coarse grained isolation
- Limited scale (n = 4096) - Large fault domain (STP)
+ Physical isolation
+ fool proof
+ L2 isolation
+ somewhat soft Cabling

## Slide 7: Isolation options: L3 with Security Groups
Security Groups or Virtual Firewall
- Difficult to combine provider policies and user policies
- Management of rules
- Impact of group membership modification
- Aggregation/summarization difficult/impossible
+ no/minimal infrastructure requirement
+ good for user policies (ip tables)

## Slide 8: Isolation Options: Virtual L2 Networks
Cloud Fabric
QA
Prod
Other
Networks
+ L2 isolation
+ compatible with large scale networks
+ can be fully automated
+ firewall can be interposed between virtual networks
Virtual Networks using Software Defined Networks
+ Can complement L3 isolation
+ large number of networks (n>4096)
- Tunnel overhead
- L2 size limited by # of tunnels and their mgt
Overlay 1
Overlay n

## Slide 9: SDN “levels”
Virtual Switches
Overlay Networks
Physical Switches
Traffic Engineering
ARP + L2 protocols
OSPF/ECMP,…
Virtual + Physical switches
Overlay Networks

## Slide 10: Implementation using openstack + Nicira NVP v1.0
Nicira
controllers
Nicira
Service
Nodes
N
vswitch
gtw-xxxx
M
Active Gateway
vswitch
Hypervisor
C
Eth1/vlan 1
vif
Eth0/vlan 2
S
Q
Eth1/vlan 1
Eth0/vlan 2
N
vswitch
gtw-xxxx
gtw-xxxx
M
Standby Gateway
10.9.0.1
10.9.0.10
10.9.160.0/24
10.9.161.0/24
10.9.160.1
10.9.161.1
Nicira
Service
Nodes
Nicira
controllers
Corp
Internet
QA
Tenant networks : 10.9.160.0/20
trunk
10.9.0.0/20 ->10.9.0.10
From 10.9.160.0/24 default->10.9.0.1 From 10.9.161.0/24 default->10.9.0.1
default->10.9.2.1
K
A
N:Nova-network+dnsmasq
C:Nova-compute
S:Nova-scheduler
M:Metadata
K:Ubuntu + KVM
A:Nova-api
Q:Quantum
Infrastructure/Internal
Infrastructure/External
Virtual network

## Slide 11: Implementation using openstack + Nicira NVP v2.0

## Slide 12: Gateway connections

## Slide 13: Openvswitch deployments
Infrastructure (Physical)
Virtualized
Bare Metal
eth0
vif0
vswitch
vswitch
eth0
External (Physical)
vif0
vif1
Gateway
QoS for drop precedence
Bare Metal
eth0
eth0
Bare Metal
Future
vswitch
eth1
eth0
vif0
vswitch
Switch